## Slide 1: Process Dynamics & Control

## Slide 2: Process Dynamics & Control (CH 61016)
Class Teacher: 1. Prof Amar Nath Samanta
2. Prof Amiya K Jana
Class TA
Mr. Shubham Raj Mr. Guru Bhattacharya
Mr. Vishal Kamble
Class Timing
Wednesday : 10 AM to 11 AM
Thursday : 9 AM to 10 AM
Friday : 11 AM to 1 PM
Attendance
Biometric method
Institute Deregistration Rule

## Slide 3: Syllabus of PDC (my part only)
  Development Process Models
  Development of Control Relevant Models
  Review of linear Dynamics
  Development of controller and observer using state space models
  Non-linear system analysis
    Phase Plane
    Bifurcation
    Stability analysis
  Feedback linearization of nonlinear systems

## Slide 4: Process Dynamics & Control
Books:
1.Process Dynamics & Control -- Seborg, Edgar, Mellichamp
& Doyle
Process Control -- W Bequette
Process Dynamics, Modelling & Control
– B A Ogunnaike & W H Ray
4. Modern Control Engineering -- K Ogata
Software: Knowledge of MATLAB & Simulink desirable

## Slide 5: Why study Process dynamics
Let us consider a very simple example of tank level control problem
Option 1:

## Slide 6: Tank Level problem
Which configuration is better from the control view point and why?
Option 2:

## Slide 7: Benchmark Systems to be used for the course
Tank Level System
  3 tank in series
  Quadruple Tank
Continuous Stirred Tank Heater
Continuous Stirred Tank Reactor system
  Isothermal Reactor (Van de Vusse reaction)
  Non-isothermal Reactor
  Polymerization Reactor
Distillation Column
MATLAB / SIMULINK model will be developed based on nonlinear model

## Slide 8: Mathematical Model of tank level system
Control objective:
Control the 3rd tank level by manipulating pump voltage V, where F0 = K V
Add q2 input flow on the tanks 2 and set q2 as manipulated variable.
Which one is difficult to control?
Data for Simulation in Matlab/Simulink
A1, A3 = 28 cm2 A2 = 32 cm2 Vs = 3 V
a1 = 0.06725 cm2 a2 = 0.05683 cm2 a3 = 0.07089 cm2 K=3.14

## Slide 9
Transfer Function model
Define :
Linearizing around steady state value
Subtracting above from steady state equation,
 Transfer function
Where, and
Similarly,
and Transfer function
and Transfer function
Where, and for j = 2,3
So, Process Transfer function

## Slide 10: Quadruple Tank problem

## Slide 11: Quadruple Tank problem
Control Objective
Both the levels of tank1 and tank2 should be controlled by manipulating voltages to the pumps.
Data for simulation:
A1, A3 = 28 cm2
A2, A4 = 32 cm2
a1, a3 = 0.071 cm2
a2, a4 = 0.057 cm2
k1, k2 = 3.33, 3.35
v1, v2 = 3.0, 3.0
γ1, γ2 = 0.7, 0.6

## Slide 12
Jacketed heated stirred tank
Assumptions:
  Constant hold-up in tank and jacket
  Constant heat capacities and densities
  Incompressible flow
Parameter and Steady State Values
F = 30 l/min; Fjs = 50 l/min; T0 = 150C; TJin = 930C; V = 300 l; Vj = 30 l;
= 1 Kcal/K l; = 1.384 ; UA = 100 Kcal/min K; Ts = 600C ; TJ = 73.5 0C

## Slide 13: Continuous Stirred Tank Reactor
Assumption:
Exit Condition = Reactor Condition
Isothermal Reaction
Constant volume, i.e, Fin = Fout=F
Only reactant A in feed is consumed, i.e, other reactant is in large excess. No product in the feed
Fin
Fout

## Slide 14: Continuous Stirred Tank Reactor
Constant volume : dV/dt = 0
Dynamic model
Since our objective is to control CB, the reduced order model should be
)
)
Data for the CSTR
V = 1 l
F = 78 l/h
CAf = 10 mol/l
kl = 50 h-1
k2 = 100 h-1
k3 = 10 l.mol-1.h-1

## Slide 15
What is the Process Gain at these points ?

## Slide 16: Non-Isothermal Jacketed CSTR
parameter | case 1 | case 2 | case 3
F/V, hr-1 | 1 | 1 | 1
k0, hr-1 | 14,825*3600 | 9,703*3600 | 18,194*3600
(-DH), kcal/kgmol | 5215 | 5960 | 8195
E, kcal/kgmol | 11,843 | 11,843 | 11,843
rcp, kcal/(m3 oC) | 500 | 500 | 500
Tf, oC | 25 | 25 | 25
CAf, kgmol/m3 | 10 | 10 | 10
UA/V, kcal/(m3 oC hr) | 250 | 150 | 750
TC, oC | 25 | 25 | 25

## Slide 17
Case 1
Case 2
Steady State for case 2
CA T
1 8.564 311.2
2 5.518 339.1
3 2.359 368.1

## Slide 18: Styrene Polymerization Reactor
Initiator Conc
Monomer Conc
Reactor Temp
Jacket Temp.
The dissociation, propagation and termination
Rate constants follow Arrhenius law :
for I =d, p or t

## Slide 19
Steady State Heat Power vs Reactor Temperature
1
2
3

## Slide 20
Phase Portrait
3
2 (unstable)
1