## Slide 1: Process Dynamics & Control

## Slide 2: Development of Mathematical Model
Motivation:
  Develop understanding of process
  Build a mathematical hypothesis of process mechanisms
  Match observed process behavior
  useful in design, optimization and control of process

## Slide 3: Development of Mathematical Model
Motivation:
  Develop understanding of process
  Build a mathematical hypothesis of process mechanisms
  Match observed process behavior
  useful in design, optimization and control of process
Control:
  Interested in description of process dynamics
    Dynamic model is used to predict how process responds to given input
    Tells us how to react

## Slide 4: Development of Mathematical Model
Mathematical Modeling of a process require
Understanding of the process
Writing conservation balance for Mass, Momentum and Energy
Writing closure equations, i.e, constitutive relationships defining equilibrium and rate parameters
Devising solution technique

## Slide 5: What kind of model do we need?
Dynamic vs. Steady-state
Steady-state
  Variables not a function of time
  useful for design calculation

## Slide 6: What kind of model do we need?
Dynamic vs. Steady-state
Steady-state
  Variables not a function of time
  useful for design calculation
Dynamic
  Variables are a function of time
  Control requires dynamic model

## Slide 7: What kind of model do we need?
Experimental vs Theoretical
Experimental
  Derived from tests performed on actual process
  Simpler model forms
  Easier to manipulate

## Slide 8: What kind of model do we need?
Experimental vs Theoretical
Experimental
  Derived from tests performed on actual process
  Simpler model forms
  Easier to manipulate
Theoretical
  Application of fundamental laws of physics and chemistry
  more complex but provides understanding
  Required in design stages

## Slide 9: What kind of model do we need?
Empirical vs. Mechanistic models
Empirical Models
  only local representation of the process (no extrapolation)
  model only as good as the data
  do not rely on underlying mechanisms
  Fit specific function to match process

## Slide 10: What kind of model do we need?
Empirical vs. Mechanistic models
Empirical Models
  only local representation of the process (no extrapolation)
  model only as good as the data
  do not rely on underlying mechanisms
  Fit specific function to match process
Mechanistic Models
  Rely on our understanding of a process
  Derived from first principles
  Observing laws of conservation of
    Mass
    Energy
    Momentum
  Useful for simulation and exploration of new operating conditions
  May contain unknown constants that must be estimated

## Slide 11: What kind of model do we need?
Linear vs Nonlinear
Linear
  basis for most industrial control
  simpler model form, easy to identify
  easy to design controller
  poor prediction, adequate control

## Slide 12: What kind of model do we need?
Linear vs Nonlinear
Linear
  basis for most industrial control
  simpler model form, easy to identify
  easy to design controller
  poor prediction, adequate control
Nonlinear
  Reality
  more complex and difficult to identify
  need state-of-the-art controller design techniques to do the job
  better prediction and control

## Slide 13: What kind of model do we need?
In existing processes, we rely on
  Dynamic models obtained from experiments
  Usually of an empirical nature
  Linear
In new applications (or difficult problems)
  Focus on mechanistic modeling
  Dynamic models derived from theory
  Nonlinear

## Slide 14: General modeling procedure
Identify modeling objectives
  end use of model (e.g. control)
Identify fundamental quantities of interest
  Mass, Energy and/or Momentum
Identify boundaries
Apply fundamental physical and chemical laws
  Mass, Energy and/or Momentum balances
Make appropriate assumptions (Simplify)
  ideality (e.g. isothermal, adiabatic, ideal gas, no friction, incompressible flow, etc,…)
Write down energy, mass and momentum balances
  develop the model equations

## Slide 15: General modeling procedure
Check model consistency
  do we have more unknowns than equations
Determine unknown constants
  e.g. friction coefficients, fluid density and viscosity
Solve model equations
  typically nonlinear ordinary (or partial) differential equations
  initial value problems
Check the validity of the model
  compare to process behavior

## Slide 16: Benchmark Systems to be used for the course
Tank Level System
  3 tank in series
  Quadruple Tank
Continuous Stirred Tank Heater
Continuous Stirred Tank Reactor system
  Isothermal Reactor (Van de Vusse reaction)
  Non-isothermal Reactor
  Polymerization Reactor
Distillation Column
MATLAB / SIMULINK model will be developed based on nonlinear model

## Slide 17: Mathematical Model of tank level system
Control objective:
Control the 3rd tank level by manipulating pump voltage V, where F0 = K V
Add q2 input flow on the tanks 2 and set q2 as manipulated variable.
Which one is difficult to control?
Data for Simulation in Matlab/Simulink
A1, A3 = 28 cm2 A2 = 32 cm2 Vs = 3 V
a1 = 0.06725 cm2 a2 = 0.05683 cm2 a3 = 0.07089 cm2 K=3.14

## Slide 18
Transfer Function model
Define :
Linearizing around steady state value
Subtracting above from steady state equation,
 Transfer function
Where, and
Similarly,
and Transfer function
and Transfer function
Where, and for j = 2,3
So, Process Transfer function

## Slide 19: Quadruple Tank problem

## Slide 20: Quadruple Tank problem
Control Objective
Both the levels of tank1 and tank2 should be controlled by manipulating voltages to the pumps.
Data for simulation:
A1, A3 = 28 cm2
A2, A4 = 32 cm2
a1, a3 = 0.071 cm2
a2, a4 = 0.057 cm2
k1, k2 = 3.33, 3.35
v1, v2 = 3.0, 3.0
γ1, γ2 = 0.7, 0.6

## Slide 21
Jacketed heated stirred tank
Assumptions:
  Constant hold-up in tank and jacket
  Constant heat capacities and densities
  Incompressible flow
Parameter and Steady State Values
F = 30 l/min; Fjs = 50 l/min; T0 = 150C; TJin = 930C; V = 300 l; Vj = 30 l;
= 1 Kcal/K l; = 1.384 ; UA = 100 Kcal/min K; Ts = 600C ; TJ = 73.5 0C

## Slide 22: Continuous Stirred Tank Reactor
Assumption:
Exit Condition = Reactor Condition
Isothermal Reaction
Constant volume, i.e, Fin = Fout=F
Only reactant A in feed is consumed, i.e, other reactant is in large excess. No product in the feed
Fin
Fout

## Slide 23: Continuous Stirred Tank Reactor
Constant volume : dV/dt = 0
Dynamic model
Since our objective is to control CB, the reduced order model should be
)
)
Data for the CSTR
V = 1 l
F = 78 l/h
CAf = 10 mol/l
kl = 50 h-1
k2 = 100 h-1
k3 = 10 l.mol-1.h-1

## Slide 24
What is the Process Gain at these points ?

## Slide 25: Non-Isothermal Jacketed CSTR
parameter | case 1 | case 2 | case 3
F/V, hr-1 | 1 | 1 | 1
k0, hr-1 | 14,825*3600 | 9,703*3600 | 18,194*3600
(-DH), kcal/kgmol | 5215 | 5960 | 8195
E, kcal/kgmol | 11,843 | 11,843 | 11,843
rcp, kcal/(m3 oC) | 500 | 500 | 500
Tf, oC | 25 | 25 | 25
CAf, kgmol/m3 | 10 | 10 | 10
UA/V, kcal/(m3 oC hr) | 250 | 150 | 750
TC, oC | 25 | 25 | 25

## Slide 26
Case 1
Case 2
Steady State for case 2
CA T
1 8.564 311.2
2 5.518 339.1
3 2.359 368.1

## Slide 27: Styrene Polymerization Reactor
Initiator Conc
Monomer Conc
Reactor Temp
Jacket Temp.
The dissociation, propagation and termination
Rate constants follow Arrhenius law :
for I =d, p or t

## Slide 28
Steady State Heat Power vs Reactor Temperature
1
2
3

## Slide 29
Phase Portrait
3
2 (unstable)
1